## Slide 2: CONTENTS
System summary
System configuration
Device Specifications
Screenshots
  Dashboard
  Monitoring
  Controls
  Statistical Analysis
  Settings
  Mobile

## Slide 3: 1. System Summary
  Wireless street light control system will provide efficient management of the equipment because it does not require any cabling connection and onsite service. This solution enable remote dimming/ON-OFF control using GSM and ZIGBEE wireless technology. This can significantly reduce the cost and time spent on operations and maintenance in your facilities.
Monitoring
Control
Statistical Analysis
• Statistical analysis of error conditions
by table and chart
• Daily and monthly chart for errors
(Print, Saving as PDF/EXCEL file)
Management
• System access permission, group settings
• User’s access history
• Management of RTU devices
• System settings
• Alarm monitoring
(Lamp ON/OFF, Battery info, Alarm status,
communication status)
• Total dashboard monitoring
(Intuitive interface)
• Web-based total monitoring system
• Remote control of road lighting by
individual, group permission
• Remote control by map search
• ON/OF, dimming control by time setting
• Remote control by mobile phone

## Slide 4: 2. System configuration
GSM network
App Server
Remote control
GSM Modem
RTU Router
Solar Lighting
Group #1
Management
. . . N
Wireless RTU
Gateway
Internet
Internet
.
.
.
Group #N
Wireless RTU
Solar Lighting
Solar Lighting

## Slide 5: 3. Device Specifications
RTU Router / Wireless RTU
    Product applications : Data transmission to
    Web monitoring server
    Size: 125mm (Width) × 90mm (Vertical) × 33 (Thickness) mm
    Display: 2 Lines CLCD
    External interface : RS-485 1Port, RS232 1Port,
    RJ-45 Ethernet 1Port, Micro USB debugger 1Port
    Wireless module: ZIGBEE module
    Memory : 2G Micro SD Memory
    Operating temperature : 0 - 80 °C
    Power : DC IN 6V ~ 9V 1.5A
    Manufacturing country : Made in Korea

## Slide 6: 4. Screen shot
1) Main – Login
Wireless street light control system will provide efficient management of the equipment because it does not require

## Slide 7: 4. Screen shot
2) Dashboard
Wireless street light control system will provide efficient management of
Remote control of road lighting by individual, group permission
Remote control by map search
ON/OF, dimming control by time setting
Remote control by mobile phone

## Slide 8: 4. Screen shot
3) Monitoring > Map Search > Location Detail
UpdateTemplate
Template
CatCat

## Slide 9: 4. Screen shot
3) Monitoring > Map Search > Location Detail
UpdateTemplate
Template
CatCat

## Slide 10: 4. Screen shot
3) Monitoring > Image Map Search
UpdateTemplate
Template
CatCat

## Slide 11: 4. Screen shot
3) Monitoring > Image Map Search > Device List
UpdateTemplate
Template
CatCat

## Slide 12: 4. Screen shot
3) Monitoring > Image Map Search > Device List > Device Detail
UpdateTemplate
Template
CatCat

## Slide 13: 4. Screen shot
3) Monitoring > Alarm History
UpdateTemplate
Template
CatCat

## Slide 14: 4. Screen shot
4) Control > Group control
UpdateTemplate
Template
CatCat

## Slide 15: 4. Screen shot
5) Statistical Analysis > Alarm reporty
UpdateTemplate
Template
CatCat

## Slide 16: 4. Screen shot
5) Statistical Analysis > Chart of Alarm status
UpdateTemplate
Template
CatCat

## Slide 17: 4. Screen shot
6) Settings > Manage members
UpdateTemplate
Template
CatCat

## Slide 18: 4. Screen shot
7) Mobile > Login
UpdateTemplate
Template
CatCat

## Slide 19: 4. Screen shot
7) Mobile > Dashboard
UpdateTemplate
Template
CatCat

## Slide 20: 4. Screen shot
7) Mobile > Monitoring
UpdateTemplate
Template
CatCat

## Slide 21: 4. Screen shot
7) Mobile > Statistical Analysis
UpdateTemplate
Template
CatCat